## Slide 1: CRUISE: Cache Replacement and Utility-Aware Scheduling
Aamer Jaleel, Hashem H. Najaf-abadi, Samantika Subramaniam,
Simon Steely Jr., Joel Emer
Intel Corporation, VSSAD
Aamer.Jaleel@intel.com
Architectural Support for Programming Languages and Operating Systems (ASPLOS 2012)

## Slide 2: Motivation
  Shared last-level cache (LLC) common with increasing # of cores
  # concurrent applications   contention for shared cache 
Core 0
L1
Core 1
L1
LLC
Core 0
L1
L2
Core 1
L1
L2
Core 2
L1
L2
Core 3
L1
L2
LLC
Core 0
L1
LLC
Single Core
( SMT )
Dual Core
( ST/SMT )
Quad-Core
( ST/SMT )
Notes: Shared caches are common and becoming even more so with increasing number of cores. As the number of concurrent applications taking advantage of the number of cores increases, the contention for the shared cache increases. It is imperative that the shared cache be managed efficiently to achieve high performance.

## Slide 3: Problems with LRU-Managed Shared Caches
  Conventional LRU policy allocates resources based on rate of demand
    Applications that have no cache benefit cause destructive cache interference
Misses Per 1000 Instr (under LRU)
soplex
h264ref
soplex
0
25
50
75
100
Cache Occupancy Under LRU Replacement
(2MB Shared Cache)
h264ref
Notes: 3. May be better to have a punch line – Unlike other work, we do not reserve cache for each application, so we do not do cache partitioning”

## Slide 4: Addressing Shared Cache Performance
  Conventional LRU policy allocates resources based on rate of demand
    Applications that have no cache benefit cause destructive cache interference
  State-of-Art Solutions:
    Improve Cache Replacement (HW)
    Modify Memory Allocation (SW)
    Intelligent Application Scheduling (SW)
Misses Per 1000 Instr (under LRU)
soplex
h264ref
soplex
0
25
50
75
100
Cache Occupancy Under LRU Replacement
(2MB Shared Cache)
h264ref
Notes: 3. May be better to have a punch line – Unlike other work, we do not reserve cache for each application, so we do not do cache partitioning”

## Slide 5: HW Techniques for Improving Shared Caches
  Modify cache replacement policy
  Goal: Allocate cache resources based on cache utility NOT demand
LLC
C0
C1
LRU
LLC
C0
C1
Intelligent
LLC Replacement
Notes: (e.g. UCP, DIP, TADIP, PIPP, SDBP, DRRIP, SHiP, GPA)

## Slide 6: SW Techniques for Improving Shared Caches I
  Modify OS memory allocation policy
  Goal: Allocate pages to different cache sets to minimize interference
LLC
C0
C1
LLC
C0
C1
LRU
LRU
Intelligent Memory
Allocator (OS)

## Slide 7: SW Techniques for Improving Shared Caches II
  Modify scheduling policy using Operating System (OS) or hypervisor
  Goal: Intelligently co-schedule applications to minimize contention
LLC0
C0
C1
LLC1
C2
C3
LLC0
C0
C1
LLC1
C2
C3
LRU-managed LLC
LRU-managed LLC
Notes: If you have a system with more than one LLC (which could be a single socket or multi-socket)

## Slide 8: SW Techniques for Improving Shared Caches
Three possible schedules:
    A, B | C, D
    A, C | B, D
    A, D | B, C
4.9
5.5
6.3
LLC0
C0
C1
LLC1
C2
C3
A
B
C
D
Worst Schedule
Optimal Schedule
~30%
Throughput
Chart: 
(4-core CMP, 3-level hierarchy, LRU-managed LLC)
Baseline System
Optimal / Worst Schedule
~9% On Average

## Slide 9: Interactions Between Co-Scheduling and Replacement
  Question:
  Is intelligent co-scheduling necessary with improved cache replacement policies?
    Existing co-scheduling proposals evaluated on LRU-managed LLCs
  DRRIP Cache Replacement [ Jaleel et al, ISCA’10 ]
Notes: Mention DRRIP requires less hardware than LRU but performs better than LRU

## Slide 10: Interactions Between Optimal Co-Scheduling and Replacement
Chart: Optimal / Worst Schedule ( LRU )
| 1.0008770349000031 | 1.0105791340000001 | 1.0352711559999968
Category 1 | 1.0184 | 1.0107 | 1.021
Category 2 | 1.0173 | 1.024 | 1.0068 | 1.0437 | 1.0705 | 1.0403 | 1.0116
Category 3 | 1.0958 | 1.1157 | 1.0453 | 1.0814 | 1.0861 | 1.1487 | 1.1972
Category 4 | 1.0583 | 1.1063 | 1.0423 | 1.0851 | 1.126 | 1.1914 | 1.2102 | 1.1584 | 1.1459
Category I: No need for intelligent
co-schedule under both LRU/DRRIP
Category II: Require intelligent
co-schedule only under LRU
Category III: Require intelligent
co-schedule only under DRRIP
Category IV: Require intelligent
co-schedule under both LRU/DRRIP
(4-core CMP, 3-level hierarchy, per-workload comparison
1365 4-core multi-programmed workloads)

## Slide 11: Interactions Between Optimal Co-Scheduling and Replacement
Chart: Optimalmal / Worst Schedule ( LRU )
Category 1 | 1.0184 | 1.0107 | 1.021
Category 2 | 1.0173 | 1.024 | 1.0068 | 1.0437 | 1.0705 | 1.0403 | 1.0116
Category 3 | 1.0958 | 1.1157 | 1.0453 | 1.0814 | 1.0861 | 1.1487 | 1.1972
Category 4 | 1.0583 | 1.1063 | 1.0423 | 1.0851 | 1.126 | 1.1914 | 1.2102 | 1.1584 | 1.1459
  Observation: Need for Intelligent Co-Scheduling is Function of Replacement Policy
(4-core CMP, 3-level hierarchy, per-workload comparison
1365 4-core multi-programmed workloads)
Category I: No need for intelligent
co-schedule under both LRU/DRRIP
Category II: Require intelligent
co-schedule only under LRU
Category III: Require intelligent
co-schedule only under DRRIP
Category IV: Require intelligent
co-schedule under both LRU/DRRIP

## Slide 12: Interactions Between Optimal Co-Scheduling and Replacement
Chart: Optimalmal / Worst Schedule ( LRU )
Category 1 | 1.0184 | 1.0107 | 1.021
Category 2 | 1.0173 | 1.024 | 1.0068 | 1.0437 | 1.0705 | 1.0403 | 1.0116
Category 3 | 1.0958 | 1.1157 | 1.0453 | 1.0814 | 1.0861 | 1.1487 | 1.1972
Category 4 | 1.0583 | 1.1063 | 1.0423 | 1.0851 | 1.126 | 1.1914 | 1.2102 | 1.1584 | 1.1459
Category II: Require intelligent
co-schedule only under LRU
LLC0
C0
C1
LLC1
C2
C3
LRU-managed LLCs
(4-core CMP, 3-level hierarchy, per-workload comparison
1365 4-core multi-programmed workloads)

## Slide 13: Interactions Between Optimal Co-Scheduling and Replacement
Chart: Optimalmal / Worst Schedule ( LRU )
Category 1 | 1.0184 | 1.0107 | 1.021
Category 2 | 1.0173 | 1.024 | 1.0068 | 1.0437 | 1.0705 | 1.0403 | 1.0116
Category 3 | 1.0958 | 1.1157 | 1.0453 | 1.0814 | 1.0861 | 1.1487 | 1.1972
Category 4 | 1.0583 | 1.1063 | 1.0423 | 1.0851 | 1.126 | 1.1914 | 1.2102 | 1.1584 | 1.1459
Category II: Require intelligent
co-schedule only under LRU
LLC0
C0
C1
LLC1
C2
C3
(4-core CMP, 3-level hierarchy, per-workload comparison
1365 4-core multi-programmed workloads)
LRU-managed LLCs

## Slide 14: Interactions Between Optimal Co-Scheduling and Replacement
Chart: Optimalmal / Worst Schedule ( LRU )
Category 1 | 1.0184 | 1.0107 | 1.021
Category 2 | 1.0173 | 1.024 | 1.0068 | 1.0437 | 1.0705 | 1.0403 | 1.0116
Category 3 | 1.0958 | 1.1157 | 1.0453 | 1.0814 | 1.0861 | 1.1487 | 1.1972
Category 4 | 1.0583 | 1.1063 | 1.0423 | 1.0851 | 1.126 | 1.1914 | 1.2102 | 1.1584 | 1.1459
Category II: Require intelligent
co-schedule only under LRU
  No Re-Scheduling Necessary for Category II Workloads in DRRIP-managed LLCs
LLC0
C0
C1
LLC1
C2
C3
(4-core CMP, 3-level hierarchy, per-workload comparison
1365 4-core multi-programmed workloads)
DRRIP-managed LLCs

## Slide 15: Opportunity for Intelligent Application Co-Scheduling
  Prior Art:
    Evaluated using inefficient cache policies (i.e. LRU replacement)
  Proposal: Cache Replacement and Utility-aware Scheduling:
    Understand how apps access the LLC (in isolation)
    Schedule applications based on how they can impact each other
      ( Keep LLC replacement policy in mind )
Notes:     Co-scheduling policies are based on application memory intensity
    Not quite optimal due to inadequate application characterization

## Slide 16: Memory Diversity of Applications (In Isolation)
LLC
Core 0
L2
Core 1
L2
CCF
Core Cache Fitting
(e.g. povray*)
LLC
Core 0
L2
Core 1
L2
LLCFR
LLC Friendly
(e.g. bzip2*)
LLC
Core 2
L2
Core 3
L2
LLCT
LLC Thrashing
(e.g. bwaves*)
LLC
Core 0
L2
Core 1
L2
LLCF
LLC Fitting
(e.g. sphinx3*)
*Assuming a 4MB shared LLC

## Slide 17: Cache Replacement and Utility-aware Scheduling (CRUISE)
LLC
  Core Cache Fitting (CCF) Apps:
    Infrequently access the LLC
    Do not rely on LLC for performance
  Co-scheduling multiple CCF jobs on same LLC “wastes” that LLC
  Best to spread CCF applications across available LLCs
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
CCF
CCF

## Slide 18: Cache Replacement and Utility-aware Scheduling (CRUISE)
LLC
  LLC Thrashing (LLCT) Apps:
    Frequently access the LLC
    Do not benefit at all from the LLC
  Under LRU, LLCT apps degrade performance of other applications
    Co-schedule LLCT with LLCT apps
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCT
LLCT

## Slide 19: Cache Replacement and Utility-aware Scheduling (CRUISE)
LLC
  LLC Thrashing (LLCT) Apps:
    Frequently access the LLC
    Do not benefit at all from the LLC
  Under DRRIP, LLCT apps do not degrade performance of co-scheduled apps
    Best to spread LLCT apps across available LLCs to efficiently utilize cache resources
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCT
LLCT

## Slide 20: Cache Replacement and Utility-aware Scheduling (CRUISE)
LLC
  LLC Fitting (LLCF) Apps:
    Frequently access the LLC
    Require majority of LLC
    Behave like LLCT apps if they do not receive majority of LLC
  Best to co-schedule LLCF with CCF applications (if present)
    If no CCF app, schedule with LLCF/LLCT
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCF
LLCF
CCF
Notes: Co-scheduling LLCF apps with any other app can degrade system performance significantly.

## Slide 21: Cache Replacement and Utility-aware Scheduling (CRUISE)
LLC
  LLC Friendly (LLCFR) Apps:
    Rely on LLC for performance
    Can share LLC with similar apps
  Co-scheduling multiple LLCFR jobs on same LLC will not result in suboptimal performance
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCFR
LLCFR

## Slide 22: CRUISE for LRU-managed Caches (CRUISE-L)
  Applications:
  Co-schedule apps as follows:
    Co-schedule LLCT apps with LLCT apps
    Spread CCF applications across LLCs
    Co-schedule LLCF apps with CCF
    Fill LLCFR apps onto free cores
LLC
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCT
LLCT
LLCF
CCF
LLCT
LLCT
LLCF
CCF

## Slide 23: CRUISE for DRRIP-managed Caches (CRUISE-D)
LLCFR
  Applications:
  Co-schedule apps as follows:
    Spread LLCT apps across LLCs
    Spread CCF apps across LLCs
    Co-schedule LLCF with CCF/LLCT apps
    Fill LLCFR apps onto free cores
LLC
Core 0
L2
Core 1
L2
LLC
Core 2
L2
Core 3
L2
LLCT
CCF
LLCT
LLCT
LLCFR
CCF
LLCT

## Slide 24: Experimental Methodology
  System Model:
    4-wide OoO processor (Core i7 type)
    3-level memory hierarchy (Core i7 type)
    Application Scheduler
  Workloads
    Multi-programmed combinations of SPEC CPU2006 applications
    ~1400 4-core multi-programmed workloads (2 cores/LLC)
    ~6400 8-core multi-programmed workloads (2 cores/LLC, 4 cores/LLC)

## Slide 25: Experimental Methodology
  System Model:
    4-wide OoO processor (Core i7 type)
    3-level memory hierarchy (Core i7 type)
    Application Scheduler
  Workloads
    Multi-programmed combinations of SPEC CPU2006 applications
    ~1400 4-core multi-programmed workloads (2 cores/LLC)
    ~6400 8-core multi-programmed workloads (2 cores/LLC, 4 cores/LLC)
LLC0
C0
C1
LLC1
C2
C3
A
B
C
D
Baseline System

## Slide 26: CRUISE Performance on Shared Caches
Chart: 
| LRU-managed LLC | DRRIP-managed LLC
Random | 1.04 | 1.0446
CRUISE-L | 1.0794 | 1.0371
CRUISE-D | 1.0255 | 1.0749
Distributed Intensity | 1.0357 | 1.0382
Optimal | 1.0921 | 1.0813
(4-core CMP, 3-level hierarchy, averaged across all 1365 multi-programmed workload mixes)
Performance Relative to
Worst Schedule
  CRUISE provides near-optimal performance
  Optimal co-scheduling decision is a function of LLC replacement policy
C R U I S E - L
C R U I S E - D
O P T I M A L
O P T I M A L
(ASPLOS’10)

## Slide 27: Classifying Application Cache Utility in Isolation
  Profiling:
    Application provides memory intensity at run time
  HW Performance Counters:
    Assume isolated cache behavior same as shared cache behavior
    Periodically pause adjacent cores at runtime
    Proposal: Runtime Isolated Cache Estimator (RICE)
      Architecture support to estimate isolated cache behavior while still sharing the LLC

x
x
x
  How Do You Know Application Classification at Run Time?

## Slide 28: Runtime Isolated Cache Estimator (RICE)
< P0, P1, P2, P3 >
  Assume a cache shared by 2 applications: APP0 APP1
High-Level View of Cache
Set-Level View of Cache
Monitor isolated cache behavior. Only APP0 fills to these sets, all other apps bypass these sets
Follower Sets
APP0
APP1
+
+
Access
Access
Miss
Miss
Monitor isolated cache behavior. Only APP1 fills to these sets, all other apps bypass these sets
32 sets per APP
15-bit hit/miss cntrs
Counters to compute
isolated hit/miss rate
(apki, mpki)

## Slide 29: Runtime Isolated Cache Estimator (RICE)
< P0, P1, P2, P3 >
  Assume a cache shared by 2 applications: APP0 APP1
High-Level View of Cache
Set-Level View of Cache
Follower Sets
APP0
APP0
APP1
APP1
+
+
+
+
Access-F
Access-H
Access-F
Access-H
Miss-F
Miss-H
Miss-F
Miss-H
Monitor isolated cache behavior if only half the cache available. Only APP0 fills to half the ways in the sets. All other apps use these sets
Needed to classify LLCF applications.
32 sets per APP
15-bit hit/miss cntrs
Counters to compute
isolated hit/miss rate
(apki, mpki)

## Slide 30: Performance of CRUISE using RICE Classifier
Chart: 
Performance Relative to
Worst Schedule
  CRUISE using Dynamic RICE Classifier Within 1-2% of Optimal
(ASPLOS’10)

## Slide 31: Summary
  Optimal application co-scheduling is an important problem
    Useful for future multi-core processors and virtualization technologies
  Co-scheduling decisions are function of replacement policy
  Our Proposal:
    Cache Replacement and Utility-aware Scheduling (CRUISE)
    Architecture support for estimating isolated cache behavior (RICE)
  CRUISE is scalable and performs similar to optimal co-scheduling
    RICE requires negligible hardware overhead

## Slide 32
Q&A