## Slide 1: Scheduling Heterogeneous Multi-Cores through Performance Impact Estimation (PIE)
ISCA 2012 presentation - June 11th 2012
Kenzo Van Craeynest,
Lieven Eeckhout
Aamer Jaleel,
Paolo Narvaez,
Joel Emer
Notes: MI

## Slide 2: Single-ISA heterogeneous multi-cores
small power-efficient cores
big high-performance cores
6/11/2012
2
B
S
B
B
…
S
S
S
…
  Multiple core types
    representing different power/performance trade-offs
  Well-established power benefits [Kumar et al. MICRO’03, ISCA’04]
  Big.LITTLE and Kal-El

## Slide 3: The effectiveness of heterogeneous multi-cores depends on workload-to-core mapping
small power-efficient cores
big high-performance cores
6/11/2012
3
?
Application threads
B
S
B
B
…
S
S
S
…
throughput
power
energy
EDP
fairness
scalable
flexible

## Slide 4: Envisioning a scalable, flexible and multi-objective scheduling algorithm
estimated performance on small core
estimated performance on big core
6/11/2012
4
S
B
scheduler
optimization criteria
workload-to-core mapping

## Slide 5: Commonly used scheduling practice
  Profiling
  Sampling
  Significant part of prior art uses idea:
    memory-intensive applications mostly wait for memory
    schedule on small core
      small performance decrease
      big power savings
compute
waiting for memory
schedule on small core
time
longer execution time
6/11/2012
5
memory-dominance scheduling
Notes: A significant part of prior art uses this insight to base scheduling decision on.

## Slide 6: Observation: Memory-intensive applications should not always be scheduled on the small core
Chart: small-core slowdown
CPI_base | 0.26433 | 0.27326 | 0.27416 | 0.29668 | 0.28918 | 0.27427 | 0.30484 | 0.26738 | 0.27151 | 0.25124 | 0.26836 | 0.27161 | 0.2621 | 0.25106 | 0.26198 | 0.27307 | 0.25279 | 0.25097 | 0.25069 | 0.25349 | 0.27144 | 0.26285 | 0.25041 | 0.25501 | 0.2508 | 0.25707 | 0.25 | 0.25001
CPI_mem | 0.64353 | 0.49146 | 0.26778 | 0.98858 | 0.02715 | 0.05127 | 0.03809 | 0.00187 | 0.01675 | 0.00248 | 0.72545 | 0.03003 | 0.08364 | 0.0009 | 0.16136 | 0.00161 | 0.00015 | 6e-05 | 0.00375 | 0.00112 | 0.24478 | 8e-05 | 0.00133 | 0.71009 | 0.0034 | 0.27127 | 0.16684 | 7e-05
small-core slowdown | 1.3552 | 1.4719 | 1.5139 | 1.5498 | 1.67 | 1.6945 | 1.7157 | 1.7515 | 1.7869 | 1.8251 | 1.9069 | 1.9688 | 1.9925 | 2.0108 | 2.0511 | 2.0548 | 2.0761 | 2.1036 | 2.138 | 2.1865 | 2.2526 | 2.2564 | 2.3142 | 2.4726 | 2.558 | 2.8431 | 3.4999 | 3.5895
Small-core slowdown can be big or small for both memory-intensive and compute-intensive applications
Kenzo Van Craeynest
6/11/2012
6

## Slide 7: Need to account for MLP in memory-intensive applications
out-of-order execution
time
issue loads
compute
core stalls: waiting for memory
time
in-order execution: MLP not preserved
time
in-order execution:
Kenzo Van Craeynest
6/11/2012
7
Chart: small-core slowdown
CPI_base | 0.26433 | 0.27326 | 0.27416 | 0.29668 | 0.28918 | 0.27427 | 0.30484 | 0.26738 | 0.27151 | 0.25124 | 0.26836 | 0.27161 | 0.2621 | 0.25106 | 0.26198 | 0.27307 | 0.25279 | 0.25097 | 0.25069 | 0.25349 | 0.27144 | 0.26285 | 0.25041 | 0.25501 | 0.2508 | 0.25707 | 0.25 | 0.25001
CPI_mem | 0.64353 | 0.49146 | 0.26778 | 0.98858 | 0.02715 | 0.05127 | 0.03809 | 0.00187 | 0.01675 | 0.00248 | 0.72545 | 0.03003 | 0.08364 | 0.0009 | 0.16136 | 0.00161 | 0.00015 | 6e-05 | 0.00375 | 0.00112 | 0.24478 | 8e-05 | 0.00133 | 0.71009 | 0.0034 | 0.27127 | 0.16684 | 7e-05
small-core slowdown | 1.3552 | 1.4719 | 1.5139 | 1.5498 | 1.67 | 1.6945 | 1.7157 | 1.7515 | 1.7869 | 1.8251 | 1.9069 | 1.9688 | 1.9925 | 2.0108 | 2.0511 | 2.0548 | 2.0761 | 2.1036 | 2.138 | 2.1865 | 2.2526 | 2.2564 | 2.3142 | 2.4726 | 2.558 | 2.8431 | 3.4999 | 3.5895
intuition
MLP preserved
Notes: Make title shorter, but say the same thing
Add graph from last slide with arrows

## Slide 8: What about compute-intensive applications?
Chart: small-core slowdown
CPI_base | 0.26433 | 0.27326 | 0.27416 | 0.29668 | 0.28918 | 0.27427 | 0.30484 | 0.26738 | 0.27151 | 0.25124 | 0.26836 | 0.27161 | 0.2621 | 0.25106 | 0.26198 | 0.27307 | 0.25279 | 0.25097 | 0.25069 | 0.25349 | 0.27144 | 0.26285 | 0.25041 | 0.25501 | 0.2508 | 0.25707 | 0.25 | 0.25001
CPI_mem | 0.64353 | 0.49146 | 0.26778 | 0.98858 | 0.02715 | 0.05127 | 0.03809 | 0.00187 | 0.01675 | 0.00248 | 0.72545 | 0.03003 | 0.08364 | 0.0009 | 0.16136 | 0.00161 | 0.00015 | 6e-05 | 0.00375 | 0.00112 | 0.24478 | 8e-05 | 0.00133 | 0.71009 | 0.0034 | 0.27127 | 0.16684 | 7e-05
small-core slowdown | 1.3552 | 1.4719 | 1.5139 | 1.5498 | 1.67 | 1.6945 | 1.7157 | 1.7515 | 1.7869 | 1.8251 | 1.9069 | 1.9688 | 1.9925 | 2.0108 | 2.0511 | 2.0548 | 2.0761 | 2.1036 | 2.138 | 2.1865 | 2.2526 | 2.2564 | 2.3142 | 2.4726 | 2.558 | 2.8431 | 3.4999 | 3.5895
Kenzo Van Craeynest
6/11/2012
8
Both MLP and ILP are contributing factors for the small-core slowdown
Notes: Unlike prior art that looks at memory-intensity alone, we do take into account cpi_base. This graph shows that this is very important

## Slide 9: Performance Impact Estimation (PIE)
CPIbig
MLPbig
ILPbig
CPIsmall
MLPsmall
ILPsmall
  estimating performance if the workload were to run on a different core type
6/11/2012
9
CPIbig
CPIsmall
S
B

## Slide 10: Performance Impact Estimation (PIE)
CPIbig
MLPbig
ILPbig
CPIsmall
MLPsmall
ILPsmall
  Determine where application spends its execution time
6/11/2012
10
CPIbig
CPIsmall
S
B
Notes: Color code the ILP and MLP

## Slide 11: Performance Impact Estimation (PIE)
CPIbig
MLPbig
ILPbig
CPIsmall
MLPsmall
ILPsmall
6/11/2012
11
CPIbig
ILP change
CPIsmall
MLP change
S
B
  Determine where application spends its execution time
  Use change in MLP exposed to predict change in CPImem
  Use change in ILP exposed to predict change in CPIbase
Notes: Color code the ILP and MLP

## Slide 12: Formal representation of the PIE Model
    Estimate big core performance while running on small core
    Estimate small core performance while running on big core
6/11/2012
12
predict

## Slide 13: Running on small, predicting CPIbase,big
Kenzo Van Craeynest
6/11/2012
13
    A balanced big (out-of-order) core should be able to dispatch approximately issue_width (Wbig) instructions per cycle in the absence of miss events.
predicted big core
CPI
small core

## Slide 14: Running on small, predicting MLPbig
Out-of-order execution:
mem | x | x | x | mem | … | mem | x
ROB size
head
Prob[ insn is a memory access ] = misses_per_instruction
MLPbig = average number of memory accesses in the ROB
= misses_per_instruction * ROB_size
Kenzo Van Craeynest
6/11/2012
14
ROB:
predicted big core
CPI
small core

## Slide 15: Formal representation of the PIE Model
    Estimate big core performance while running on small core
    Estimate small core performance while running on big core
6/11/2012
15

## Slide 16: Running on big, predicting CPIbase,small
1 | 2 | 3 | 4
Kenzo Van Craeynest
6/11/2012
16
  *Small core = 4-wide in-order
We use a model based on the probability that x instructions will execute
Example: Prob[executing two instructions per cycle] ?
insn 2 cannot depend on insn 1
insn 3 must depend on insn 1 or insn 2
= dependency distance is > 1
= dependency distance is <= 2
big core
CPI
predicted small core

## Slide 17: Running on big, predicting MLPsmall
In-order execution (stall on use):
mem | 1 | 2 | 3 | … | … | … | x
dependency distance (D)
consumer
small = average number of memory accesses in the ‘instruction window’
= misses_per_instruction * Daverage
Kenzo Van Craeynest
6/11/2012
17
independent instructions
producer
big core
CPI
predicted small core

## Slide 18: Inputs for PIE model
6/11/2012
18
  Need hardware counters for
    per-thread cache misses
    memory stall cycles
  Profile information for which PIE needs additional support
    recording dependency distance distribution: 5 counters
    tracking dependencies: 4 bits per architectural register
    roughly 15-20 bytes of storage per core

## Slide 19: Using PIE to determine a static schedule
    1 in-order core / 1 out-of-order core
    Private last-level cache
    Selection of scheduling-sensitive workload mixes
Kenzo Van Craeynest
6/11/2012
19
Chart: system throughput relative to worst-case
| optimal | random | memory-dominance | PIE
 | 0.17046 | 0.085231 | 0.093737 | 0.14239
84%
Notes: Use bar charts instead

## Slide 20: Evaluating dynamic PIE scheduling
    1 in-order core / 1 out-of-order core
    Migration period: 2.5ms
    Private last-level caches
Kenzo Van Craeynest
6/11/2012
20
Chart: sorted two-program workloads
See paper for
alternative cache hierarchies
different core counts
different small-to-big core ratios
PIE outperforms memory-dominance scheduling by 5.5% and sampling-based scheduling by 8.7%

## Slide 21: Evaluating dynamic PIE scheduling
    1 in-order core / 1 out-of-order core
    Migration period: 2.5ms
    Shared last-level cache
Chart: sorted two-program workloads
Kenzo Van Craeynest
6/11/2012
21
See paper for
alternative cache hierarchies
different core counts
different small-to-big core ratios
5.5%
8.7%

## Slide 22: Conclusions and contributions
  Using memory intensity, MLP or ILP alone as an indicator to guide workload scheduling decisions is insufficient
Kenzo Van Craeynest
6/11/2012
22
predicted small core
big core
CPI
predicted big core
CPI
small core
MLP
ILP
Each core can individually estimate performance on the other core types
MLP
ILP

## Slide 23: Conclusions and contributions
    PIE is scalable with core count
    Requires limited hardware to collect profile information at runtime
    Evaluate PIE for a variety of systems with varying core counts and cache configurations
    PIE improves system performance by an average of 5.5% over recent state-of-the-art scheduling proposals and by 8.7% over a sampling-based scheduling policy
Kenzo Van Craeynest
6/11/2012
23

## Slide 24
Questions?
Kenzo Van Craeynest
6/11/2012
24

## Slide 25: Dynamic Thread Migration: Sampling
  Previous results encourage a sampling based approach
    frequent migration doesn’t hurt performance (much)
  Periodically force thread on each core type and measure performance difference
B
S
time
time
…
…
forced migration
evaluation
evaluation
forced migration

## Slide 26: Dynamic Thread Migration: Sampling
  Previous results encourage a sampling based aproach
    frequent migration doesn’t hurt performance (much)
  Periodically force thread on each core type and measure performance difference
    doesn’t scale well: big core quickly becomes bottleneck
    very few insight is gained: observation only
    slower to adapt to phase changes
B
S
time
time
…
…
S
time
…

## Slide 27: State of the art
  Profile based [Chen and John]
    needs offline information
  Sampling based [Kumar et al., Becchi and Crowley]
    does not scale well with increasing core (type) count
    migration overhead
    slow to adapt to phase changes
  A proxy to predict relative performance
    stall cycles
    execution speed
    cpu utilization
    memory stall cycles
  Biggest core first scheduling [Li at al.]
    Maximize utilization of the big core
Kenzo Van Craeynest
6/11/2012
27

## Slide 28: PIE accurately predicts the relative performance differences between the big and small cores
Chart: small-core slowdown
| GemsFDTD | astar.B | astar.r | bwaves | bzip2.c | bzip2.c | bzip2.l | bzip2.p | bzip2.s | bzip2.t | cactusADM | calculix | dealII | gamess.c | gamess.h | gamess.t | gcc.166 | gcc.200 | gcc.c | gcc.cp-decl | gcc.expr | gcc.expr2 | gcc.g23 | gcc.s04 | gcc.s | gobmk.t | gobmk.n | gobmk.s | gobmk.t | gromacs | h264.f_ref | h264.f_base | h264ref.sss | hmmer.n | hmmer.r | lbm | leslie3d | libquantum | mcf.ref | milc.su3 | namd | omnetpp | perl.c | perl.diff | perl.split | povray | sjeng | soplex.pds | soplex | sphinx3.an4 | tonto | wrf.r | xalancbmk | zeusmp
actual | 2.8431 | 3.4999 | 3.5895 | 2.2526 | 1.9815 | 2.1865 | 2.2564 | 2.0108 | 2.558 | 2.3142 | 2.4764 | 1.6923 | 1.8251 | 2 | 2.0761 | 2.0576 | 1.4719 | 1.5288 | 1.4891 | 1.7157 | 2.2979 | 1.4286 | 1.5139 | 2.0529 | 1.67 | 1.8672 | 1.7869 | 1.8188 | 1.7154 | 1.7564 | 2.0548 | 2.0772 | 2.1625 | 2.138 | 2.1036 | 2.0511 | 2.2251 | 1.3552 | 1.5498 | 2.4726 | 2.2538 | 1.9069 | 1.6072 | 1.7266 | 1.6945 | 1.9573 | 1.9688 | 2.9781 | 2.5977 | 2.0342 | 1.7515 | 2.1368 | 1.9925 | 2.3811
predicted big->small | 2.4451 | 2.2849 | 2.7452 | 1.5312 | 1.9056 | 2.0875 | 2.1317 | 2.1509 | 2.272 | 2.3556 | 2.3771 | 1.5226 | 1.917 | 2.0646 | 2.1003 | 2.1391 | 1.4982 | 1.559 | 1.5169 | 1.7984 | 1.969 | 1.4559 | 1.6113 | 2.1167 | 1.8245 | 2.1506 | 2.0344 | 1.8292 | 2.0159 | 1.6863 | 1.8624 | 2.0016 | 1.9237 | 2.2051 | 2.1988 | 2.038 | 1.8559 | 1.3454 | 1.5307 | 2.24 | 2.1771 | 1.737 | 1.7884 | 1.858 | 1.8632 | 1.8881 | 2.159 | 2.3759 | 2.1796 | 1.7504 | 1.8374 | 1.9827 | 1.7629 | 1.8409
predicted small->big | 2.4386 | 1.934 | 2.039 | 1.2213 | 1.7008 | 1.6941 | 1.8681 | 1.4559 | 1.7453 | 1.7676 | 2.3448 | 1.273 | 1.7874 | 1.9856 | 1.9123 | 2.0187 | 1.4361 | 1.4773 | 1.5354 | 1.8562 | 1.787 | 1.6698 | 1.5464 | 1.8066 | 1.7997 | 2.0753 | 1.9415 | 1.598 | 1.9272 | 1.5223 | 1.9507 | 2.0376 | 2.0889 | 1.9533 | 2.0313 | 1.9354 | 1.7015 | 1.2014 | 1.499 | 2.2372 | 2.0128 | 1.6922 | 1.8054 | 1.809 | 1.791 | 1.7718 | 2.1049 | 2.3132 | 2.1508 | 1.6624 | 1.8752 | 1.9019 | 1.6141 | 1.6537
  Estimate big(small)-core performance while executing the workload on a small (big) core
  Average absolute prediction error of 9% and 13%
6/11/2012
28

## Slide 29: Static scheduling using PIE
  Heterogeneous (1 big,1 small) multi-core
    e.g., ARM’s big.LITTLE
    PIE to determine the workload-to-core mapping
  Memory-dominance scheduling:
    always scheduling memory-intensive workloads on the small core.
6/11/2012
29
Chart: sorted two-program workloads

## Slide 30: Static scheduling using PIE
  4 core heterogeneous multi-core
    e.g., NVidia’s Kal-El
    PIE to determine the workload-to-core mapping
  Memory-dominance scheduling:
    always scheduling memory-intensive workloads on the small core.
6/11/2012
30
Chart: sorted four-program workloads (3 Big 1 Small)
Chart: sorted four-program workloads (1Big 3 Small)

## Slide 31: Performance impact varies across applications
Simulation based study
Chart: relative performance
| libquantum | gcc.166 | gcc.g23 | mcf.ref | gcc.s | perl.split | gcc.cp-decl | tonto | gobmk.n | dealII | omnetpp | sjeng | xalancbmk | bzip2.p | lbm | h264.f_ref | gamess.h | hmmer.r | hmmer.n | bzip2.c | bwaves | bzip2.l | bzip2.t | milc.su3 | bzip2.s | GemsFDTD | astar.B | astar.r
in-order | 1.2505 | 1.2813 | 1.0143 | 2.3214 | 0.675 | 0.64085 | 0.75086 | 0.49719 | 0.59658 | 0.46511 | 2.1336 | 0.60808 | 1.007 | 0.51993 | 0.90749 | 0.59642 | 0.54131 | 0.52881 | 0.54661 | 0.57583 | 1.1794 | 0.69885 | 0.59374 | 2.5196 | 0.67973 | 1.5842 | 1.5526 | 0.92741
out-of-order | 0.92272 | 0.87052 | 0.66997 | 1.4979 | 0.40419 | 0.3782 | 0.43764 | 0.28386 | 0.33387 | 0.25484 | 1.1189 | 0.30886 | 0.50538 | 0.25857 | 0.44245 | 0.29025 | 0.26074 | 0.25138 | 0.25566 | 0.26336 | 0.52358 | 0.30972 | 0.25656 | 1.019 | 0.26573 | 0.5572 | 0.44362 | 0.25837
relative performance | 1.3552 | 1.4719 | 1.5139 | 1.5498 | 1.67 | 1.6945 | 1.7157 | 1.7515 | 1.7869 | 1.8251 | 1.9069 | 1.9688 | 1.9925 | 2.0108 | 2.0511 | 2.0548 | 2.0761 | 2.1036 | 2.138 | 2.1865 | 2.2526 | 2.2564 | 2.3142 | 2.4726 | 2.558 | 2.8431 | 3.4999 | 3.5895
6/11/2012
31
  Scheduling for heterogeneous multi-cores is a significant problem
small
big
relative performance

## Slide 32: Both ILP and MLP are important for scheduling
Chart: 
small-core slowdown | 2.1036 | 2.2564 | 3.5895 | 2 | 2.0761 | 1.9573 | 2.0108 | 2.1865 | 2.3142 | 2.0548 | 1.7266 | 2.0576 | 1.7515 | 2.2538 | 2.1625 | 1.8251 | 2.558 | 2.0772 | 2.138 | 1.8672 | 2.0529 | 2.2979 | 1.7564 | 1.6923 | 1.7869 | 1.67 | 1.7154 | 1.7157 | 1.9688 | 1.9815 | 1.6945 | 1.8188 | 2.3811 | 1.6072 | 1.9925 | 2.1368 | 2.0342 | 1.4286 | 2.0511 | 3.4999 | 1.5139 | 2.4764 | 1.4891 | 2.2526 | 2.8431 | 1.5288 | 2.2251 | 1.4719 | 2.5977 | 2.9781 | 1.9069 | 1.5498 | 2.4726 | 1.3552
ILP ratio | 2.0663 | 2.1276 | 2.6581 | 1.9852 | 1.9762 | 1.891 | 1.8537 | 1.9948 | 2.0805 | 1.8466 | 1.8508 | 2.0219 | 1.7867 | 2.1606 | 1.9018 | 1.7958 | 2.1185 | 2.0216 | 2.0592 | 1.9955 | 1.9281 | 1.8587 | 1.6391 | 1.7613 | 1.954 | 1.8375 | 1.9987 | 1.8421 | 2.0336 | 2.0357 | 1.8588 | 1.9439 | 1.8854 | 1.8319 | 2.098 | 2.015 | 1.8334 | 1.5048 | 2.2156 | 2.6393 | 1.958 | 1.8877 | 1.742 | 1.8535 | 1.8488 | 1.9712 | 1.9983 | 1.8953 | 2.0406 | 2.1107 | 1.9144 | 1.9029 | 1.6376 | 2.0251
MLP ratio | 0.98913 | 1.125 | 1.2833 | 0.99275 | 1.262 | 1.2313 | 0.50909 | 0.78058 | 0.84709 | 1.6535 | 0.90102 | 1.2531 | 1.2858 | 1.1471 | 2.132 | 1.365 | 1.0641 | 1.5893 | 1.0185 | 1.1321 | 1.2772 | 1.1372 | 1.0329 | 1.0418 | 1.1534 | 1.1483 | 1.1265 | 1.2252 | 1.4332 | 0.90054 | 1.2154 | 0.52031 | 1.3339 | 1.12 | 1.2226 | 1.5241 | 1.4352 | 1.0601 | 1.4941 | 1.6151 | 1.1764 | 2.7427 | 1.1761 | 0.94494 | 2.7748 | 1.1803 | 1.5391 | 1.1886 | 2.1803 | 2.3586 | 1.6024 | 1.3529 | 2.3989 | 0.90429
memory-bound
compute-bound

## Slide 33: Quantifying migration overhead
  1 application, 2 identical cores
  Migrate application every x ms
  Shared last-level cache (4MB)
Chart: relative performance
| gromacs.gromacs | perlbench.diffmail | dealII.ref | namd.namd | xalancbmk.ref | tonto.tonto | astar.BigLakes2048 | gobmk.trevord | gobmk.nngs | povray.ref | gobmk.score2 | gobmk.trevorc | bzip2.text | gcc.scilab | h264ref.sss_main | h264ref.foreman_ref_main | calculix.hyperviscoplastic | hmmer.nph3 | h264ref.foreman_ref_baseline | gamess.h2ocu2+ | perlbench.checkspam | bzip2.source | bzip2.combined | gamess.triazolium | gcc.g23 | gcc.200 | gcc.s04 | sjeng.ref | astar.rivers | gamess.cytosine | hmmer.retro | zeusmp.zeusmp | bzip2.chicken | bzip2.liberty | gcc.c-typeck | bzip2.program | gcc.166 | omnetpp.omnetpp | sphinx3.an4 | cactusADM.benchADM | gcc.expr2 | leslie3d.leslie3d | wrf.rsl | soplex.pds-50 | perlbench.splitmail | mcf.ref | gcc.cp-decl | bwaves.bwaves | GemsFDTD.ref | soplex.ref | gcc.expr | milc.su3imp | lbm.lbm | libquantum.ref
0.5 ms | -0.03327 | -0.031625 | -0.020688 | -0.019183 | -0.017716 | -0.017026 | -0.01643 | -0.016066 | -0.016062 | -0.015903 | -0.015795 | -0.014915 | -0.014819 | -0.01458 | -0.014535 | -0.014461 | -0.014167 | -0.013364 | -0.012443 | -0.011442 | -0.011314 | -0.01077 | -0.010264 | -0.010219 | -0.0094948 | -0.0089837 | -0.0088314 | -0.0084694 | -0.0082865 | -0.0077462 | -0.0067699 | -0.0062616 | -0.0060363 | -0.0060205 | -0.0058378 | -0.0056278 | -0.005013 | -0.0042706 | -0.0041179 | -0.0040601 | -0.0037814 | -0.0035417 | -0.0035294 | -0.0034306 | -0.0027955 | -0.0018498 | -0.0018305 | -0.0015202 | -0.0013886 | -0.0009956 | -0.00014757 | -0.00010729 | -7.7854e-05 | -1.2426e-05
1.0 ms | -0.016551 | -0.015747 | -0.013311 | -0.011303 | -0.0084059 | -0.0099954 | -0.0082183 | -0.0086469 | -0.0083686 | -0.0082428 | -0.0098695 | -0.0075463 | -0.0075798 | -0.0075528 | -0.0080264 | -0.0082703 | -0.0069933 | -0.0065449 | -0.0067821 | -0.0062561 | -0.0057461 | -0.0053723 | -0.0058771 | -0.0058047 | -0.0046421 | -0.0042983 | -0.0043093 | -0.0045061 | -0.0045082 | -0.0043706 | -0.0033755 | -0.0031072 | -0.0032703 | -0.0030665 | -0.0031867 | -0.0026916 | -0.0026155 | -0.0019875 | -0.0019179 | -0.00203 | -0.0019196 | -0.0020009 | -0.0017532 | -0.00168 | -0.0016526 | -0.00086174 | -0.00090159 | -0.00074381 | -0.00070895 | -0.00045891 | -5.903e-05 | -5.3643e-05 | -2.7805e-05 | -6.2132e-06
2.5 ms | -0.0065082 | -0.006453 | -0.0064649 | -0.0054092 | -0.0027721 | -0.0043267 | -0.0032747 | -0.0038075 | -0.0032124 | -0.0035079 | -0.0046102 | -0.0029669 | -0.0028343 | -0.0030382 | -0.003317 | -0.0033841 | -0.0027631 | -0.0025015 | -0.0029266 | -0.0030635 | -0.0024562 | -0.0020934 | -0.0023944 | -0.0029305 | -0.0017024 | -0.0016774 | -0.0018443 | -0.0018419 | -0.0021253 | -0.0021073 | -0.0013389 | -0.001335 | -0.0013254 | -0.0012097 | -0.0016161 | -0.0010352 | -0.00099136 | -0.00078681 | -0.00075589 | -0.00084585 | -0.00072853 | -0.0011473 | -0.00060482 | -0.00068565 | -0.00089578 | -0.00029467 | -0.00035517 | -0.00028513 | -0.00028784 | -0.00018473 | -2.9515e-05 | -3.9338e-05 | -2.2244e-05 | -2.0711e-06
5.0 ms | -0.0032167 | -0.0032019 | -0.0035398 | -0.0029383 | -0.0011724 | -0.0022034 | -0.0016248 | -0.0019393 | -0.0016144 | -0.0017933 | -0.0023301 | -0.0015641 | -0.0013767 | -0.0014339 | -0.0015646 | -0.0013536 | -0.0014581 | -0.0011651 | -0.0013669 | -0.0018455 | -0.001176 | -0.0007945 | -0.0011721 | -0.0016531 | -0.00073712 | -0.00082256 | -0.00095762 | -0.00087161 | -0.0012022 | -0.0012292 | -0.00066002 | -0.00054346 | -0.00063389 | -0.00064707 | -0.0010441 | -0.00047055 | -0.00035155 | -0.00041387 | -0.00041743 | -0.00043138 | -0.00034692 | -0.00088404 | -0.00033686 | -0.00033458 | -0.00038611 | -0.00011391 | -0.00017759 | -0.00013637 | -0.00023454 | -8.7504e-05 | -9.8383e-06 | -1.7881e-05 | -1.6683e-05 | -2.0711e-06
10 ms | -0.0014774 | -0.0016748 | -0.0016745 | -0.0015192 | -0.00044712 | -0.00088136 | -0.00081238 | -0.0010141 | -0.0010049 | -0.00094383 | -0.0011317 | -0.00075786 | -0.00074502 | -0.00066726 | -0.0007823 | -0.00082538 | -0.00064802 | -0.0007196 | -0.00070099 | -0.001015 | -0.00050613 | -0.00035311 | -0.00065301 | -0.00086413 | -0.00030713 | -0.00032257 | -0.00046107 | -0.00041114 | -0.00056889 | -0.00064389 | -0.00033944 | -0.00027173 | -0.00033135 | -0.0003798 | -0.0007808 | -0.00018822 | -0.00023202 | -0.0002274 | -0.00021436 | -0.00022838 | -0.00021972 | -0.00046835 | -0.00016843 | -0.00017907 | -0.00032433 | -7.1812e-05 | -9.5623e-05 | -8.6778e-05 | -0.00017591 | -7.5837e-05 | -9.8383e-06 | -7.1524e-06 | -1.1122e-05 | -2.0711e-06
25 ms | -0.00063586 | -0.00073889 | -0.00052991 | -0.00061772 | -0.00028814 | -0.00050077 | -0.00031488 | -0.00035584 | -0.00039537 | -0.00044045 | -0.00041608 | -0.00025799 | -0.00021055 | -0.00028394 | -0.00031292 | -0.00034666 | -0.00023401 | -0.00023987 | -0.00029792 | -0.00044291 | -0.00011909 | -0.00025222 | -0.00021767 | -0.00037571 | -0.00013163 | -0.00017742 | -0.0001596 | -0.00011512 | -0.00028981 | -0.00029268 | -0.00015086 | -0.00010633 | -0.00011525 | -0.00015473 | -0.00059922 | -7.5288e-05 | -0.00014062 | -8.1864e-05 | -0.00014667 | -7.6127e-05 | -0.00018502 | -0.00018013 | -6.8903e-05 | -9.8959e-05 | -0.00012356 | -2.7239e-05 | -4.0981e-05 | -3.4091e-05 | -7.7292e-05 | -2.3334e-05 | 0 | -3.5762e-06 | -5.561e-06 | 0
50 ms | -9.3509e-05 | -0.00037766 | -0.00036034 | -0.00026712 | -0.00023846 | -0.00024037 | -0.00015114 | -0.00016013 | -0.00019768 | -0.00023596 | -0.00029958 | -0.000129 | -6.4785e-05 | -0.00015617 | -0.00017211 | -0.00016508 | -0.000135 | -8.5666e-05 | -0.00012267 | -0.00018455 | -7.4431e-05 | -3.7833e-05 | -3.3488e-05 | -0.00015028 | -1.755e-05 | -6.4515e-05 | -5.3201e-05 | -9.8673e-05 | -9.6604e-05 | -0.00013658 | -5.6573e-05 | -4.7257e-05 | -5.7626e-05 | -5.6267e-05 | -7.2632e-05 | -5.6466e-05 | -6.3278e-05 | -5.0028e-05 | -3.3846e-05 | -3.3834e-05 | -0.00019659 | -7.4825e-05 | -3.0624e-05 | -4.4767e-05 | -0.00010811 | -1.2381e-05 | -2.7321e-05 | -1.7046e-05 | -3.9978e-05 | -1.1667e-05 | 0 | 0 | -5.561e-06 | 0
6/11/2012
Kenzo Van Craeynest, VSSAD intern
Kenzo Van Craeynest
6/11/2012
33

## Slide 34: Caveat: high performance degradation if data not preserved in LLC
  1 application, 2 identical cores
  Migrate application every x ms
  Private last-level cache (4MB), LLC powered off
Chart: relative performance
| calculix.hyperviscoplastic | sphinx3.an4 | bzip2.liberty | gcc.cp-decl | bzip2.source | gcc.scilab | gromacs.gromacs | astar.rivers | bzip2.text | bzip2.combined | bzip2.chicken | h264ref.foreman_ref_baseline | bzip2.program | gcc.expr | hmmer.retro | gcc.g23 | perlbench.splitmail | hmmer.nph3 | xalancbmk.ref | omnetpp.omnetpp | gcc.200 | h264ref.foreman_ref_main | h264ref.sss_main | soplex.pds-50 | perlbench.diffmail | gcc.c-typeck | dealII.ref | zeusmp.zeusmp | gcc.166 | gobmk.trevorc | perlbench.checkspam | gobmk.nngs | namd.namd | gcc.s04 | gamess.triazolium | astar.BigLakes2048 | gobmk.score2 | gobmk.trevord | tonto.tonto | leslie3d.leslie3d | povray.ref | GemsFDTD.ref | gamess.h2ocu2+ | mcf.ref | sjeng.ref | wrf.rsl | gcc.expr2 | cactusADM.benchADM | gamess.cytosine | soplex.ref | bwaves.bwaves | lbm.lbm | milc.su3imp | libquantum.ref
0.5 ms | -3.1051 | -1.73 | -1.6804 | -1.6733 | -0.86518 | -0.83179 | -0.74566 | -0.67901 | -0.63283 | -0.58802 | -0.56876 | -0.48271 | -0.47808 | -0.46566 | -0.43429 | -0.41261 | -0.39329 | -0.36023 | -0.35371 | -0.34436 | -0.33194 | -0.3268 | -0.32398 | -0.31434 | -0.30495 | -0.29821 | -0.29015 | -0.2712 | -0.2281 | -0.20581 | -0.18176 | -0.17619 | -0.1615 | -0.15519 | -0.15296 | -0.14015 | -0.10214 | -0.098285 | -0.089575 | -0.088467 | -0.084517 | -0.075677 | -0.073275 | -0.065039 | -0.058862 | -0.051982 | -0.049885 | -0.043165 | -0.033455 | -0.021039 | -0.011914 | -0.0064932 | -0.0025231 | -0.00018875
1.0 ms | -1.6646 | -1.6868 | -1.4848 | -1.6585 | -0.53326 | -0.48771 | -0.35185 | -0.62161 | -0.50475 | -0.47086 | -0.49477 | -0.43329 | -0.41556 | -0.18373 | -0.37447 | -0.24979 | -0.19575 | -0.29292 | -0.27049 | -0.2811 | -0.27892 | -0.28453 | -0.28725 | -0.23374 | -0.14102 | -0.26672 | -0.20484 | -0.23445 | -0.18557 | -0.13553 | -0.10996 | -0.10979 | -0.10098 | -0.072863 | -0.13054 | -0.07313 | -0.068233 | -0.053663 | -0.063103 | -0.072564 | -0.04488 | -0.056418 | -0.042798 | -0.058747 | -0.035104 | -0.044321 | -0.037091 | -0.037007 | -0.019753 | -0.016573 | -0.0065782 | -0.003178 | -0.0023128 | -0.0001057
2.5 ms | -0.37055 | -0.71654 | -1.0195 | -1.2159 | -0.22734 | -0.22203 | -0.14572 | -0.45981 | -0.36012 | -0.27162 | -0.31561 | -0.37956 | -0.29808 | -0.05781 | -0.18108 | -0.12778 | -0.095812 | -0.17941 | -0.19994 | -0.16624 | -0.2006 | -0.20338 | -0.20945 | -0.080912 | -0.057634 | -0.21375 | -0.088792 | -0.12831 | -0.14845 | -0.079648 | -0.061349 | -0.058468 | -0.052301 | -0.02825 | -0.083306 | -0.035292 | -0.031306 | -0.023711 | -0.038935 | -0.044334 | -0.01985 | -0.022589 | -0.022171 | -0.054171 | -0.017772 | -0.015528 | -0.027519 | -0.03095 | -0.0099461 | -0.0074138 | -0.0027855 | -0.0012459 | -0.0020938 | -3.7749e-05
5.0 ms | -0.1623 | -0.25743 | -0.67205 | -0.41554 | -0.12662 | -0.11708 | -0.080597 | -0.24875 | -0.23119 | -0.13716 | -0.153 | -0.23989 | -0.20292 | -0.03679 | -0.094373 | -0.057749 | -0.055929 | -0.1063 | -0.15443 | -0.074938 | -0.10666 | -0.05553 | -0.075674 | -0.040007 | -0.030293 | -0.15187 | -0.041803 | -0.061052 | -0.10312 | -0.048619 | -0.037663 | -0.035908 | -0.031156 | -0.012912 | -0.038446 | -0.022355 | -0.016356 | -0.012418 | -0.026093 | -0.01939 | -0.010736 | -0.011743 | -0.012561 | -0.032124 | -0.0105 | -0.010637 | -0.021138 | -0.017045 | -0.005286 | -0.0037196 | -0.0014999 | -0.00059125 | -0.0017609 | 7.5498e-06
10 ms | -0.069529 | -0.094084 | -0.3195 | -0.15366 | -0.073289 | -0.058305 | -0.049088 | -0.11176 | -0.116 | -0.070129 | -0.073724 | -0.14109 | -0.13942 | -0.014727 | -0.049032 | -0.032608 | -0.036423 | -0.060316 | -0.065264 | -0.035922 | -0.048041 | -0.039842 | -0.050284 | -0.02 | -0.015045 | -0.082927 | -0.022729 | -0.025672 | -0.037642 | -0.030761 | -0.021157 | -0.020774 | -0.0196 | -0.0067295 | -0.02252 | -0.013532 | -0.0082825 | -0.0064987 | -0.017196 | -0.0085709 | -0.0055866 | -0.0057819 | -0.0065209 | -0.013942 | -0.0058925 | -0.0040363 | -0.015538 | -0.0070432 | -0.002643 | -0.0032527 | -0.0007071 | -0.00026395 | -0.0014192 | 7.5498e-06
25 ms | -0.015454 | -0.017009 | -0.087278 | -0.03768 | -0.020481 | -0.011765 | -0.012134 | -0.019555 | -0.045529 | -0.010341 | -0.021912 | -0.054407 | -0.025448 | -0.0044013 | -0.010544 | -0.015724 | -0.0042805 | -0.025751 | -0.019356 | -0.0099304 | -0.0083586 | -0.0039842 | -0.03293 | -0.0039188 | -0.0041663 | -0.027947 | -0.0043857 | -0.0057978 | -0.014107 | -0.012311 | -0.0063687 | -0.007896 | -0.0045662 | -0.0012639 | -0.0076388 | -0.0023754 | -0.0037376 | -0.0021555 | -0.0081088 | -0.0029402 | -0.0022159 | -0.00099923 | -0.00065209 | -0.0041661 | -0.0020373 | -0.0010605 | -0.016575 | -0.0026563 | -0.00052165 | -0.00037551 | -0.00028927 | -8.4465e-05 | 0 | -7.5498e-06
50 ms | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Kenzo Van Craeynest
6/11/2012
34